## Slide 1: Title: Computer Architecture: Foundations and Trends
Makumi Bedan SCT212-0051/2021

## Slide 2: The Computing Revolution
1.1 Introduction

## Slide 3: A Revolution Beyond Faster Clocks: A Paradigm Shift
Unprecedented Performance Growth: For nearly two decades (mid-1980s to early 2000s), processor performance increased by roughly 52% per year. This was an extraordinary period driven by both technological improvements (smaller, faster transistors) and architectural innovations (pipelining, caches, etc.).
Driven by Technology and Architecture: It wasn't just Moore's Law (increasing transistor density). Clever architectural techniques were essential to translate those extra transistors into performance gains.
Now Facing New Challenges: This period of rapid, automatic performance improvement has ended. We've hit fundamental physical limits (power, heat).
The End of Dennard Scaling: Dennard scaling states that as transistors get smaller, power density stays constant.
New Opportunities: This "crisis" is forcing a shift to new architectural paradigms, primarily focused on parallelism.

## Slide 4: The Single-Processor Performance Wall: Why Your New Laptop Isn't That Much Faster
Historical Reliance on ILP: For years, architects focused on Instruction-Level Parallelism (ILP) – extracting parallelism within a single instruction stream (e.g., executing multiple instructions simultaneously). Techniques included pipelining, superscalar execution, out-of-order execution, and branch prediction.
Diminishing Returns from ILP: We've squeezed most of the available ILP out of typical programs. The complexity of extracting more ILP grows exponentially, and the power consumption becomes prohibitive.
Clock Speeds Have Plateaued: Increasing clock frequency was a major driver of performance. But we've hit the "power wall" – chips are generating too much heat to be cooled effectively at higher clock speeds.
The "Free Lunch" is Over: In the past, software automatically ran faster on new processors. This is no longer true. Software must be rewritten to exploit parallelism to see significant performance gains.

## Slide 5: Parallelism: The Path Forward – Many Hands Make Light Work
Exploiting parallelism is essential for continued performance gains. We must find ways to do multiple things at the same time.
Types of Application-Level Parallelism:
Data-Level Parallelism (DLP): Many data items can be processed by the same operation simultaneously. Think of applying a filter to every pixel in an image, or multiplying a vector by a scalar. This is often found in multimedia, scientific computing, and data analytics.
Task-Level Parallelism (TLP): Independent tasks can run concurrently. Think of a web server handling requests from multiple users, or a desktop computer running multiple applications. This is common in server workloads and general-purpose computing.
Distinction: DLP is often more structured and easier to exploit automatically. TLP can be more irregular and require more explicit programmer intervention.

## Slide 6: Hardware Architectures for the Parallel Era.
Four major ways hardware exploits application parallelism.
Four Architectures:
Instruction-Level Parallelism (ILP): Exploits DLP at modest levels using pipelining and speculative execution.
Vector Architectures and Graphic Processor Units (GPUs): Apply single instruction to collection of data in parallel.
Thread-Level Parallelism: Exploits DLP and TLP, allows for interaction among parallel threads.
Request-Level Parallelism: Exploits parallelism among decoupled tasks.

## Slide 7: Classes of Computers: A Diverse Landscape
1.2 Classes of Computers

## Slide 8: From Phones to Warehouses: Different Needs, Different Architectures
Personal Mobile Devices (PMDs): Smartphones, tablets. Extreme pressure on cost and energy consumption (battery life). Focus on responsiveness for interactive applications (user interface, media playback). Often use specialized hardware for graphics and media processing.
Desktop Computing: The traditional PC market. Driven by price-performance – getting the best performance for a given budget. Covers a wide range, from low-end netbooks to high-end gaming rigs. Increasingly dominated by laptops.
Servers: Powering businesses and online services. Emphasis on availability (must be up and running 24/7), scalability (ability to handle increasing workloads), and throughput (processing many requests per second). Often use multiple processors and redundant components.
Clusters/Warehouse-Scale Computers (WSCs): The "supercomputers" of the cloud era. Tens of thousands of servers working together. Extreme focus on price-performance and energy proportionality (power consumption should scale with workload). Often use commodity hardware and sophisticated software to manage failures.
Embedded Systems: Computers hidden inside other devices (cars, appliances, industrial equipment). Wide range of requirements, but often emphasize low cost, low power, and real-time performance (meeting strict deadlines).

## Slide 9: The Two Extremes: Small and Huge
Personal Mobile Devices (PMDs):
Driven by Battery Life and Size: The most critical constraints. Every milliwatt and every millimeter matters.
Media-Rich Applications: Video, audio, gaming, web browsing. These require specialized hardware acceleration (GPUs, video decoders).
Responsiveness is Critical: Users expect instant feedback. Poor responsiveness is unacceptable.
Increasingly Powerful: PMDs are approaching the capabilities of desktop computers from just a few years ago.
Warehouse-Scale Computers (WSCs):
Powering the "Cloud": The infrastructure behind services like Google Search, Facebook, Amazon, etc.
Extreme Focus on Cost and Energy Efficiency: Small improvements in efficiency translate to huge savings in operational costs (electricity bills).
Energy Proportionality: Ideal: a system consumes almost no power when idle and power scales linearly with utilization. This is a major research area

## Slide 10: Defining Computer Architecture: The Complete Picture
1.3 Defining Computer Architecture

## Slide 11: More Than Just Instructions: A Holistic View of Computer Design
Three Key Aspects
Instruction Set Architecture (ISA): The contract between software and hardware. Defines the programmer-visible state (registers, memory), the instructions the processor can execute, and how data is accessed (addressing modes). Examples: x86, ARM, MIPS. The ISA is the interface.
Organization (Microarchitecture): The implementation of the ISA. How the processor is structured internally. Includes techniques like pipelining, caching, branch prediction, out-of-order execution, and speculative execution. Different organizations can implement the same ISA (e.g., AMD and Intel both implement x86).
Hardware: The physical realization. Logic design (how the circuits are created), packaging (how the chip is connected to the outside world), power delivery, and cooling. This is where the physics meets the architecture.

## Slide 12: ISA Examples
Key Dimensions of an ISA (with more detail):
Class: Most modern ISAs are load-store architectures (only load and store instructions access memory; other operations use registers). Older designs (like x86) were register-memory architectures.
Memory Addressing: How memory locations are specified. Typically byte addressing (each byte has a unique address). Alignment requirements (e.g., a 4-byte word must start at an address divisible by 4).
Addressing Modes: Different ways to calculate the effective address of a memory operand (e.g., register indirect, displacement, indexed).
Operand Types and Sizes: Integers (8-bit, 16-bit, 32-bit, 64-bit), floating-point numbers (single-precision, double-precision), characters, etc.
Operations: Arithmetic (add, subtract, multiply, divide), logical (and, or, not), data transfer (load, store), control flow (branches, jumps, calls), floating-point operations.
Control Flow: How the program execution sequence is changed. Conditional branches (based on comparisons), unconditional jumps, procedure calls and returns.
Encoding: How instructions are represented as binary numbers. Fixed-length encoding (e.g., MIPS, ARM) simplifies instruction decoding. Variable-length encoding (e.g., x86) can save space but makes decoding more complex

## Slide 13: Technology Trends: Semiconductors
1.4 Trends in Technology

## Slide 14: The Foundation: Semiconductor Technology – The Engine of Progress
Moore's Law: Transistor density (number of transistors per unit area) doubles roughly every 18-24 months. This has been the driving force behind the computer revolution. However, the rate of increase is slowing down.
Impact:
More Transistors per Chip: Allows for more complex processors (more cores, larger caches).
Faster Transistors (to a point): Transistor switching speed generally improves with smaller feature sizes, but this improvement is also slowing down.
Wire Delays Don't Scale Well: As transistors get smaller and faster, the wires connecting them don't improve proportionally. Wire resistance and capacitance become increasingly significant, limiting performance. This is a major challenge.

## Slide 15: Technology Trends: Memory and Storage
1.4 Trends in Technology

## Slide 16: Memory and Storage: Capacity, Cost, and the Bandwidth/Latency Gap
Trends (with more detail):
DRAM: Dynamic Random Access Memory. Main memory in most computers. Capacity growth is slowing. Price per bit continues to decrease, but not as rapidly as in the past.
Flash Memory: Non-volatile memory (retains data without power). Used in SSDs, smartphones, USB drives. Rapid capacity growth. Significantly cheaper than DRAM per bit. Slower than DRAM, but faster than disk.
Disk (Magnetic): Traditional hard drives. Massive capacity. Much cheaper than DRAM or Flash per bit. Much slower than DRAM or Flash (mechanical limitations).
Key Point: Bandwidth (data transfer rate) generally improves faster than latency (access time) for all these technologies. This "bandwidth-latency gap" is a significant challenge for computer architects. Caches are a crucial technique to bridge this gap.

## Slide 17: Power and Energy: The Critical Constraint
1.5 Trends in Power and Energy in Integrated Circuits

## Slide 18: The Power Wall and Energy Efficiency: The Limits of Performance
Dynamic Power: Power consumed when transistors are switching. Proportional to :
Capacitance: The amount of charge that needs to be moved.
Voltage: Reducing voltage has a huge impact on power.
Frequency: How often transistors switch per second.
Static Power: Power consumed even when transistors are not switching (leakage current). Proportional to:
Number of transistors and Voltage
Leakage: Current that flows even when a transistor is "off." Becoming increasingly significant as transistors get smaller.
Why it Matters
Limits Clock Speeds: Higher clock speeds require more power, generating more heat. We've reached the limit of what can be cooled effectively with air cooling.
Drives Multi-Core Designs: Instead of making a single core faster (and hotter), we now use multiple, slower, more energy-efficient cores.
Impacts Battery Life (PMDs): The primary concern for mobile devices.
Huge Cost Factor for WSCs: Electricity bills are a major expense for data centers. Energy efficiency is crucial for economic viability.

## Slide 19: Techniques for Power Management
Clock Gating: Turning off the clock signal to inactive modules (e.g., the floating-point unit when it's not being used). This eliminates dynamic power consumption in those modules.
Dynamic Voltage-Frequency Scaling (DVFS): Reducing both the voltage and frequency of the processor (or parts of the processor) when full performance is not needed. This has a cubic impact on dynamic power (Voltage² * Frequency).
Low-Power Modes: Putting memory (DRAM) and storage (disks, SSDs) into low-power states when they are idle. Trade-off: it takes time to "wake up" from these modes.
Overclocking (Turbo Mode): Temporarily increasing the clock frequency above the nominal value when thermal conditions allow. Used to boost performance for short bursts. Relies on on-chip temperature sensors.
Race-to-Halt: Complete tasks quickly and then enter sleep mode

## Slide 20: Cost: The Economic Reality
1.6 Trends in Cost

## Slide 21: Cost Considerations in Computer Design: It's Not Just About Performance
Factors Affecting Cost
Time (Learning Curve): Manufacturing yield (the percentage of working chips) improves over time as the manufacturing process matures. Higher yield = lower cost.
Volume: Higher production volume leads to lower cost per unit due to economies of scale (spreading fixed costs over more units) and better purchasing power.
Commoditization: When multiple vendors offer essentially identical products (e.g., DRAM, disks), competition drives prices down.
IC Cost
Die Area is the Dominant Factor: The cost of a chip is roughly proportional to the square of the die area. Larger dies are exponentially more expensive.
Yield: The percentage of manufactured dies that actually work. Affected by defects in the manufacturing process.
Cost ≈ (Wafer Cost) / (Dies per Wafer * Die Yield) This formula highlights the importance of die area and yield.
Dies per Wafer: Depends on wafer size and die size (see formulas in the chapter).
Die Yield: A complex function of defect density, die area, and process complexity (see the Bose-Einstein formula).

## Slide 22: Cost Considerations in Computer Design: Cont.
Cost vs. Price: The selling price of a product includes not only the manufacturing cost but also R&D costs, marketing, sales, profit margins, etc.
Cost of Operation: This includes power consumption, cooling costs, and infrastructure costs (especially important for WSCs).

## Slide 23: Thank you